## Slide 1: Internet4schools – guest Wi-Fi solutions
Options for connecting adult guest users in schools that have our Protex Appliance

## Slide 2: Option1 Layer3 routed subnet
Layer 3 switch
Guest SSID = VLAN x
subnet 10.31.55.0/24
Student/Staff Managed SSID = VLAN y
subnet 10.31.45.0/24
Protex Appliance
Transparent Filter Default
= Protex:Student Filtering with SSL content inspection
Transparent Filter Location Map
10.31.55.0/24
= Staff No Man in the Middle Filtering
Transit or routing subnet VLAN z 10.255.255.0/30

## Slide 3: Option2 Layer2 connected subnets
Layer 2 switch
Guest SSID = VLAN x
subnet 10.31.55.0/24
Student/Staff Managed
SSID = VLAN y
subnet 10.31.45.0/24
Protex Appliance
Transparent Filter Default
= Protex:Student Filtering with SSL content inspection
Transparent Filter Location Map
10.31.55.0/24
= Staff No Man in the Middle Filtering
Untagged VLAN y to Protex LAN port 10.31.45.1
Untagged VLAN x to Protex DMZ port 10.31.55.1

## Slide 4: Option3 WIFI NAT MODE
Layer 2 switch
Guest SSID = DHCP/NAT Mode
Client Scope 192.168.1.0/24
AP address / NAT address 10.31.45.5
Student/Staff Managed SSID - Bridge Mode
AP address 10.31.45.5
Client scope 10.31.45.0/24 – passed through AP un-natted
Protex Appliance
Transparent Filter Default
= Protex:Student Filtering with SSL content inspection for un-natted student/staff devices
Transparent Filter Location Map
10.31.45.5
= Staff No Man in the Middle Filtering
192.168.1.x clients “hide” behind Access Point IP address
10.31.45.1